## Slide 1
HW SW Co-Design
Projuct Presentation
Presented by :
Tal Schneider
Almog As

## Slide 2
01
Chosen Benchmarks
nbody
Computer problem
N-body gravity simulation
5.4M float operations per call
Data fits fully in L1 cache
02
pyflate
Data-Movement Problem
Pure-Python bzip2 decode
127K page faults per run
35x higher cache miss rate
>
>
>
>
>
>

## Slide 3
Test Environment
Host CPU
Intel Xeon E5-2630 v3
METHODOLOGY
Guest OS
Ubuntu 22.04 LTS (KVM)
Interpreter
CPython 3.10.12 (Debug)

## Slide 4
Fixed-Work Measurment
The Problem
Default harness runs 27 processes.
Created 15.9% instruction overcount.
METHODOLOGY
Our Fix
Single worker process locked flags.
Exact same work across variants.

## Slide 5
PMU & Debug Corrections
Virtual PMU Limitations
Lacks sampling interrupts. Required explicit event profiling.
METHODOLOGY
DWARF Unwinding
Frame pointers fail on -Og builds. DWARF used instead.
Debug Allocator Noise
Excluded 18.3% profile artifacts from pyflate baseline.

## Slide 6
nbody Overview
Five-body gravitational simulation of the sun and four gas giants.
20,000 timesteps per call.
5.4 M float operations per call.
Pure CPython generic flaot obkects.
In-place list sequence writes.
>
>
>
>
NBODY BENCHMARK

## Slide 7
Instruction Bound Workload
Milliseconds per call
NBODY BENCHMARK
477
2.9G
2.54
Instructions per call
Instructions per cycle

## Slide 8
Overhead Dominated
Spent managing heap objects
NBODY BENCHMARK
88.9%
Interpreter dispatch:
Sequence element access:
Float boxing:
REAL float arithmetic:
47.1%
12.8%
12.6%
11.1%

## Slide 9
Hoist Indexed Reads
Before
v1[0] -= dx * b2m
v1[1] -= dy * b2m
v1[2] -= dz * b2m
After
NBODY OPT1
v1x, v1y, v1z = v1
v1[0] = v1x - dx * b2m
.....
Repeated generic sequence protocols
Unpacked to local variables

## Slide 10
Time per call
-10.3%
-8.5%
-53%
Instructions per call
Sequence operations
Sequence Work Halved
NBODY OPT1 REASULTS

## Slide 11
After
Math Reassociation
Before
NBODY OPT2
Generic exponentiation operator
Replaced with math.sqrt()

## Slide 12
Math saved 0.059G instructions.
Python function dispatch cost 0.166G.
+3.7%
The path to a cheaper operation can cost more than the operation itself.
A Measured Regression
NBODY OPT2 REASULTS

## Slide 13
Cython Typed Core
NBODY OPT3
Typed Arrays
Values live unboxed in registers.
Compile-Time Types
Zero Python interpreter dispatch in the hot loop.
Identical Semantics
Final energy output bit-exact.

## Slide 14
Runtime Reduction
99.2%
125x
147x
Faster overall
Fewer instructions
Interpreter Bypassed
NBODY OPT3 REASULTS
Required linear intercept calculation to remove 37% startup noise

## Slide 15
pyflate Overview
Pure-Python bzip2 decompression workload.
89,837 MTF operations per call.
145-entry Python list mutation.
Fixed MD5 digest verification.
Data-movement bound algorithm.
>
>
>
>
PYFLATE BENCHMARK

## Slide 16
Memory Bound Workload
Seconds per call
PYFLATE BENCHMARK
3.14
16.6G
127k
Instructions per call
Page fault per run

## Slide 17
List slicing, concatenation, and deallocation completely dominate the python execution path.
Interpreter dispatch:
Debug-build allocator (excluded):
Function call machinery:
List & slice ops (MTF):
29.4%
18.3%
12.2%
11.7%
MTF List Churn
PYFLATE BENCHMARK

## Slide 18
The MTF Bottleneck
3 List Slices
2 Concatenations
5 Heap Allocations
PYFLATE BENCHMARK
21,400
Instructions per byte

## Slide 19
In-Place MTF
PYFLATE OPT1
After
Before
Complete list rebuild
Two internal memmoves

## Slide 20
Time per call
-12.7%
-72%
0
MTF stage operations
Heap allocations
Stage Cost Collapsed
PYFLATE OPT1 REASULTS

## Slide 21
Table-Driven Huffman Decode
PYFLATE OPT2
Grouped symbols by code length.
Replaced linear scan loop with one dict lookup per length.
Linear Search
Slow interpreted loop
Heap Lookup
Direct length mapping

## Slide 22
Cumulative speedup
-16.2%
The Real Mechanism
PYFLATE OPT2 REASULTS
Unexpected Attribution
Dict lookups actually increased
92% gain from eliminating the interpreter loop

## Slide 23
Move-To-Front Unit
HARDWARE PROPOSAL
Fixed Working Set
256 bytes resident. Zero memory traffic.
High Utilization
Runs 89,837 times per call.
Software Proven
Opt1 proved stage value.

## Slide 24
mtf_unit: Single-Cycle Parallel Shift
HARDWARE PROPOSAL

## Slide 25
Flow & Interfaces
SOFTWARE INTEGRATION
ISA Extension
1 cycle execution (~5 ns).
Custom instruction (e.g. RISC-V custom-0).
Memory Mapped
Two bus round trips (~100-200 ns).
32-bit AXI4-Lite slave.

## Slide 26
Energy vs. Power
HARDWARE TRADE-OFFS
Peak Power
Increases during operation
Energy Per Op
Collapses by orders of magnitude
Silicon Area
Minimal cost for high impact

## Slide 27
The Amdahl Reality
Zero mismatches across 89,837 operations.
Accelerating a stage 1,294x yields a modest global limit.
1,294x
MTF Stage Speedup
1.23x
Global Benchmark Limit

## Slide 28
The Value of Profiling
PROJECT CONCLUSIONS
nbody
Only 11.1% of runtime is the arithmetic the algorithm requires.
539 interpreter instructions per float operation vs. 3.66 in C.
Opt3 proved removing interpretation yields 125x speedup.
pyflate
A data-movement workload (35x nbody's LLC miss rate).
MTF stage costs ≈21,400 instructions to move one byte.
Opt2 showed removing an interpreted search loop beat dictionary speedups.
The HW/SW Lesson
An accelerator making its target 1,294x faster only speeds up pyflate by 1.23x.
The useful result is not just target speed, but how much total runtime it removes.

## Slide 29
Big Thanks!
Questions?